## Slide 1
BIO-ACOUSTIC SENSING
WEARABLE
Non-Invasive Gesture Recognition & Haptic Feedback
Mr. Mummidi Jayanth-2303A52485
Student, CS & AI
Mr. Sakinala Yagneshwar-2303A52073
Student, CS & AI
Mr. Munigala Teja-2303A52298
Student, CS & AI
Mr. Komurevelly Prudhvi Raj-2303A52349
Student, CS & AI
SR University, Warangal, Telangana | Department of CS & AI

## Slide 2
INTRODUCTION
What is it?
A wearable bio-acoustic sensing system that detects skeletal muscle movements and joint vibrations propagated through human skin using miniaturized MEMS piezoelectric microphones — enabling touchless, screenless gesture recognition for controlling electronic devices.
The Problem it Solves
Touchscreens are unhygienic in medical/cleanroom settings
Vision-based systems need line-of-sight & raise privacy concerns
EMG wearables are sensitive to electrode placement & consume high power
Voice control fails in noisy or silent environments
92.4%
Gesture Classification Accuracy
Across 5 test participants | SVM Classifier | 300 samples/class
Key Concept
Using body-borne acoustic signals (vibrations from muscles, tendons, joints) as the sensing modality — no cameras, no electrodes, no external hardware.

## Slide 3
OBJECTIVES
01
Non-Invasive Sensing
Detect skeletal muscle & joint vibrations through skin using MEMS piezoelectric sensors — no electrodes or skin adhesives required.
02
Real-Time Gesture Recognition
Classify 10+ hand/wrist gestures with ≥90% accuracy using on-device CNN or SVM classifier with STFT/MFCC feature extraction.
03
Closed-Loop Haptic Feedback
Provide tactile confirmation to users via LRA/ERM actuators, completing the interaction loop without visual displays.
04
Privacy-Preserving HMI
Operate entirely from body-borne signals — no cameras, no external sensors, no cloud dependency for inference.
05
Accessibility & Inclusivity
Enable gesture-based control for individuals with motor disabilities, amputees, or tremors — a universal, adaptable interface.
06
Low-Power Wearable Design
Achieve ≥12 hours continuous operation with a 200–400 mAh LiPo battery using passive acoustic sensing and TinyML inference.

## Slide 4
STAKEHOLDERS
Who benefits from this technology?
Persons with Disabilities
Amputees, motor-impaired individuals, and those with tremors gain accessible, electrode-free gesture control.
AR/VR Users
Silent, peripheral-free hand/finger input for immersive environments without bulky controllers.
Medical Professionals
Contactless patient interface in operating theatres and sterile zones — hygienic and non-intrusive.
Industrial Workers
Hands-free machinery control in hazardous, noisy, or cleanroom environments.
Consumer Electronics
Wristband or glove-form wearables to control smartphones, TVs, and IoT devices silently.
Military & Defence
Silent, covert HMI for field operatives requiring hands-free communication without sound.
Smart Prosthetics
Intent detection using residual limb muscle sounds to drive prosthetic limb actuators.
Clinical Researchers
Joint health monitoring by analyzing acoustic emissions indicative of cartilage degeneration.

## Slide 5
PROGRAMMING LANGUAGES, TOOLS & SOFTWARE
Programming Languages
▸ Python 3.x — ML model training, signal processing pipeline
▸ C/C++ — Embedded firmware on ARM Cortex-M MCU
▸ JavaScript/Node.js — Web dashboard & BLE interface
ML & Signal Processing
▸ TensorFlow Lite / TinyML — On-device CNN inference
▸ Scikit-learn — SVM classifier training & evaluation
▸ NumPy / SciPy — STFT, MFCC, bandpass filter implementation
▸ Librosa — Audio/acoustic feature extraction
Hardware & Embedded
▸ STM32 (ARM Cortex-M4F) — MCU with DSP core
▸ MEMS Piezoelectric Sensors — Acoustic signal acquisition
▸ DRV2605L — Haptic feedback driver IC
▸ BLE 5.0 Module — Wireless data transmission
Development Tools
▸ Keil MDK / STM32CubeIDE — Embedded IDE
▸ Jupyter Notebook — Model training & visualization
▸ Edge Impulse — TinyML pipeline & deployment
▸ Arduino IDE — Rapid prototyping

## Slide 6
AI PROMPTS USED TO GENERATE CODES
P1
[ChatGPT / Claude] Signal acquisition & pre-processing
"Write a Python script to read MEMS sensor data from a serial port, apply a Butterworth bandpass filter (10-2000 Hz), and output the filtered signal in real time."
P2
[ChatGPT / Copilot] Feature extraction module
"Generate Python code to extract MFCC features (13 coefficients) from a sliding window (50ms, 25ms overlap) of audio/acoustic data using librosa and prepare feature vectors for SVM classification."
P3
[ChatGPT / Claude] ML classifier training
"Write a Python script to train an SVM classifier with RBF kernel on gesture MFCC feature vectors, evaluate accuracy, and export the trained model using joblib for embedded deployment."
P4
[GitHub Copilot] Embedded firmware
"Write C++ code for STM32 ARM Cortex-M4 to receive ADC samples at 8kHz, apply a fixed-point bandpass filter, compute MFCC features, and run SVM inference to output gesture class via UART."
P5
[ChatGPT] BLE & haptic feedback control
"Create a Python script using the BLE library to receive gesture classification results wirelessly from an STM32 device and trigger haptic feedback patterns based on gesture class (pinch, swipe, fist)."

## Slide 7
AI PROMPTS USED TO GENERATE CODES
Part 2 / 2
P6
[ChatGPT] Dataset collection & preprocessing
"Write a Python script to collect labelled gesture training data from a MEMS sensor via serial port, store samples as CSV with gesture class labels, and split into train/test sets for model training."
P7
[GitHub Copilot] TinyML model conversion
"Generate a TensorFlow Lite model conversion script that takes a trained Keras CNN gesture classifier and exports it as a quantized .tflite model suitable for deployment on an ARM Cortex-M4 microcontroller."
P8
[Claude AI] Web dashboard front-end
"Create a React.js web dashboard component that connects to a BLE wearable device, displays live gesture classification results, confidence scores, and gesture event history in a real-time updating table."
P9
[ChatGPT] Model evaluation & visualization
"Write Python code to evaluate gesture classifier performance — generate a confusion matrix, classification report (precision, recall, F1 per gesture class), and plot accuracy vs training samples graph using matplotlib."
P10
[Claude AI] Haptic driver firmware
"Generate C code for STM32 to control a DRV2605L haptic driver IC over I2C — implement three distinct vibration patterns (short buzz for success, double-pulse for error, long rumble for system idle) triggered by gesture class output."

## Slide 8
SYSTEM WORKFLOW FLOWCHART
1
GESTURE INITIATION
User performs hand/wrist gesture
2
BIO-ACOUSTIC ACQUISITION
MEMS piezoelectric sensors capture vibrations
3
SIGNAL CONDITIONING
Amplify → Bandpass filter (10–2000 Hz) → 16-bit ADC @ 8kHz
4
FEATURE EXTRACTION
STFT / MFCC (13 coefficients, 50ms window)
5
ML CLASSIFICATION
CNN or SVM → Gesture class + confidence score
6
DEVICE COMMAND
BLE 5.0 transmits command to connected device
7
HAPTIC FEEDBACK
LRA/ERM actuator delivers tactile confirmation
Flow: Gesture → Sensing → Processing → AI Classification → Command → Feedback

## Slide 9
FRONT-END APPLICATION VIEW
BioAcoustic Gesture Dashboard | localhost:3000
🎯 Bio-Acoustic Gesture Dashboard
Gesture
PINCH
Confidence
92.4%
Status
ACTIVE
Signal Waveform (Live)
Gesture Log
12:04:32
PINCH
92.4%
Scroll Up
12:04:28
FIST
88.1%
Play/Pause
12:04:21
SWIPE
95.0%
Next Slide
App Features
Live Waveform Monitor
Real-time acoustic signal visualization from MEMS sensors
Gesture Classification Panel
Shows detected gesture, confidence score & mapped command
Haptic Feedback Control
Configure vibration pattern intensity and duration
BLE Device Manager
Pair/unpair wearable, monitor connection status
Session Logger
Record & export gesture logs for ML model retraining

## Slide 10
PROOF OF PROMPTS GENERATING CODE
ChatGPT — Signal Processing Code
> "Write Python code for Butterworth bandpass filter 10-2000Hz for acoustic gesture data"
from scipy.signal import butter, sosfilt
import numpy as np
def butter_bandpass(lowcut, highcut, fs, order=4):
nyq = 0.5 * fs
low, high = lowcut/nyq, highcut/nyq
sos = butter(order, [low, high], btype='band',
analog=False, output='sos')
return sos
def apply_filter(data, fs=8000):
sos = butter_bandpass(10, 2000, fs)
return sosfilt(sos, data)
Claude AI — MFCC Feature Extraction
> "Generate MFCC feature extraction for gesture classification with sliding window"
import librosa, numpy as np
def extract_mfcc_features(signal, sr=8000,
n_mfcc=13, win_len=0.05, hop_len=0.025):
n_fft = int(win_len * sr)
hop = int(hop_len * sr)
mfcc = librosa.feature.mfcc(
y=signal, sr=sr,
n_mfcc=n_mfcc, n_fft=n_fft,
hop_length=hop
)
return np.mean(mfcc.T, axis=0)

## Slide 11
PROOF OF PROMPTS GENERATING CODE
Part 2 / 3
ChatGPT — Dataset Collection Script
> P6: "Write a Python script to collect labelled gesture training data from MEMS sensor via serial port, store as CSV with gesture class labels"
import serial, csv, time
from datetime import datetime
GESTURE_LABELS = ['pinch','fist','swipe',
'thumb_up','open_palm']
def collect_data(gesture, samples=300,
port='COM3', baud=115200):
ser = serial.Serial(port, baud)
rows = []
print(f'Collecting {gesture}...')
for _ in range(samples):
line = ser.readline().decode().strip()
rows.append(line.split(',') + [gesture])
return rows
with open('gesture_data.csv','w') as f:
w = csv.writer(f)
for label in GESTURE_LABELS:
data = collect_data(label)
w.writerows(data)
GitHub Copilot — TinyML Model Conversion
> P7: "Generate a TensorFlow Lite conversion script for a trained Keras CNN gesture classifier to deploy on ARM Cortex-M4"
import tensorflow as tf
import numpy as np
# Load trained Keras model
model = tf.keras.models.load_model(
'gesture_cnn.h5')
# Convert to TFLite with INT8 quantization
converter = tf.lite.TFLiteConverter
.from_keras_model(model)
converter.optimizations = [
tf.lite.Optimize.DEFAULT]
converter.target_spec.supported_ops = [
tf.lite.OpsSet.TFLITE_BUILTINS_INT8]
tflite_model = converter.convert()
open('gesture_model.tflite','wb')
.write(tflite_model)
print('Model size:', len(tflite_model),'bytes')

## Slide 12
PROOF OF PROMPTS GENERATING CODE
Part 3 / 3
Claude AI — React.js BLE Dashboard
> P8: "Create a React.js component that connects to a BLE wearable, displays live gesture results, confidence scores and gesture history"
import { useState, useEffect } from 'react';
export default function GestureDashboard() {
const [gesture, setGesture] = useState('--');
const [confidence, setConf] = useState(0);
const [log, setLog] = useState([]);
const connectBLE = async () => {
const device = await navigator.bluetooth
.requestDevice({filters:[
{name:'BioAcousticWearable'}]});
const server = await device.gatt.connect();
// Subscribe to gesture notifications
server.getPrimaryService('gesture-svc')
.then(svc => svc.getCharacteristic('gesture'))
.then(ch => ch.startNotifications())
.then(ch => ch.addEventListener(
'characteristicvaluechanged', onGesture));
};
return (<button onClick={connectBLE}>Connect</button>);
}
Claude AI — STM32 Haptic Driver (C Code)
> P10: "Generate C code for STM32 to control DRV2605L haptic driver over I2C with 3 distinct vibration patterns for gesture feedback"
#include 'drv2605l.h'
#include 'i2c.h'
#define DRV2605_ADDR 0x5A
#define REG_MODE 0x01
#define REG_WAVESEQ1 0x04
#define REG_GO 0x0C
void haptic_pattern(uint8_t pattern) {
// Pattern: 1=success, 2=error, 3=idle
uint8_t effects[] = {1, 10, 47};
I2C_Write(DRV2605_ADDR,
REG_WAVESEQ1, effects[pattern-1]);
I2C_Write(DRV2605_ADDR, REG_GO, 0x01);
}
void gesture_feedback(uint8_t gesture_id) {
if (gesture_id > 0) // Recognised
haptic_pattern(1); // Short buzz
else // Error
haptic_pattern(2); // Double pulse
}

## Slide 13
REFERENCES
1
2
Thalmann, N.M., et al. (2020). 'Gesture Recognition Using Acoustic Sensing on Wearable Devices.' IEEE Transactions on Neural Systems & Rehabilitation Engineering, 28(3), 619-628.
3
Boyali, A., & Hashimoto, N. (2016). 'Spectral collaborative representation based classification for hand gestures recognition on EMG signals.' Biomedical Signal Processing and Control, 24, 11-18.
4
Davis, S. & Mermelstein, P. (1980). 'Comparison of Parametric Representations for Monosyllabic Word Recognition in Continuously Spoken Sentences.' IEEE Transactions on ASSP, 28(4), 357-366.
5
TensorFlow Lite for Microcontrollers. (2024). Google AI Edge. https://ai.google.dev/edge/litert/microcontrollers/overview
6
Edge Impulse Documentation. (2024). Building and Deploying Embedded ML Models. https://docs.edgeimpulse.com
7
STMicroelectronics. (2023). STM32F4 Series ARM Cortex-M4 with DSP Instruction Set. Application Note AN4127. https://www.st.com
8
Texas Instruments. (2022). DRV2605L Haptic Driver for LRA and ERM with Effect Library and Smart Loop. Datasheet SLOS825E. https://www.ti.com
SR University, Warangal, Telangana | Department of CS & AI | 2024
Akhlaghi, N., et al. (2016). 'Artificial Neural Network Classification of Motor Unit Potentials in Needle EMG and Acoustic Myography.' Journal of Neural Engineering, 13(1), 016003.

## Slide 14
THANK YOU